## Slide 1: Engineering Safety in Hydrogen-Energy Applications
6th ICHS, October 19-21, 2015 – Yokohama, Japan
1 AREVA ENERGY STORAGE
2 INERIS
Audrey DUCLOS1, C. Proust2, J. Daubech2, and F. Verbecke1

## Slide 2: Content
Context
Overall objectives
State-of-the-art : European projects on Risk management
Application of ARAMIS method
Discussion
Conclusions

## Slide 3: Overview
Context
  Hydrogen technologies and applications are already introduced into the market (Fuel Cell Vehicles for instance)
  Objectively, hydrogen ignites easily and explodes violently > Safety engineering has to be particularly strong and demonstrative
Overall project objectives
  Various risk analysis methods used/developed so far in the field of hydrogen safety are reviewed and assessed
  None of them seem to be fully adapted to engineer safety on a practical daily basis
  An alternative is presented in the following

## Slide 4: State-of-the-art : European projects on Risk management
BEMHA Benchmark Exercise on Major Hazards Analysis 1988-1990
  Resulted in a overview of methodologies for chemical risk assessment in Europe
  Highlighted the strong influence of the assumptions made all along the risk assessment process
ASSURANCE Assessment of the Uncertainties in Risk Analysis of Chemical Establishment 1998-2001
  The hazard identification phase was very critical
  Quite different ranking of the accidental scenarios were obtained
  As for the scenarios’ frequency assessment, the estimates were also quite contradictory

## Slide 5
Comparison of probabilities calculated in ASSURANCE project. (Grey tanned cells contain the lower assessments. Black tanned cells contain the upper assessments)
# |  | 3 | 5 | 7
Scenario |  | Rupture or disconnection between ammonia ship and unloading arm | Rupture of a ship tank | Rupture of 20" pipe (distribution line of cryogenic tank)
Partner | 1 | 4.8 10-4 | 2.8 10-7 | 6.0 10-6
 | 2 | 4.8 10-6 | 6.4 10-10 | 1.0 10-6
 | 3 | 8.0 10-3 | 5.7 10-5 | 5.0 10-6
 | 4 | 5.0 10-3 | --- | 9.0 10-7
 | 5 | 5.4 10-5 | 2.3 10-6 | 4.0 10-7
 | 7 | 1.3 10-5 | 4.9 10-6 | 4.0 10-7
Range of deviation |  | 4.8 10-6 - 8.0 10-3 | 6.4 10-10 - 5.7 10-5 | 6.0 10-6 - 4.0 10-7

## Slide 6
International Energy Agency - Hydrogen Implementing Agreement Tasks 19 and 31 2004-present
  The overall outcomes of IEA HIA Task 19 are:
    The use of off-shore or HydroCarbon Release database is irrelevant
    > HIAD (Hydrogen Incident and Accident Database) is a valuable tool to estimate the hydrogen-associated event frequencies
    Hydrogen systems risk analysis should also reflect the importance of the safety barriers
    Safety barriers must: avoid releases, detect gas leak, remove ignition source and/or shut down and isolate part of the process
    The human factors and so the safety culture had to be integrated into risk assessment.

## Slide 7: ARAMIS (2002-2004) METHOD PRESENTATION
Accidental Risk Assessment Methodology for Industries
The ARAMIS project is based on:
  an approach by barriers: identification of all conceivable major accident scenarios + the inventory of all safety equipment impeding the development of an accident
  the final acceptability = the demonstration that the proper dimensioning of safety barriers is capable of keeping the identified risks under control
  decision making = a quantified line is drawn between acceptable and unacceptable accidents
ARAMIS contains two methods:
  MIMAH (Methodology for Identification of Major Accident Hazards) : identification of all accidental scenarios physically conceivable
  MIRAS (Methodology for the Identification of Reference Accident Scenarios) : selection the reference scenarios to be modelled and entered into the severity map

## Slide 8: APPLICATION TO AN HYDROGEN OBJECT
H2 Storage
Electrolyser
Container
Fuel Cell’s modules
DP2
Differential of pressure
DP1
Over-Flow Valve
No-return Valve
Regulator
Mode ELY
Mode FC
O2 Storage
Water Storage
Storage | Pressure | 35 | bar
 | Volume of hydrogen | 6 | m3
 | Volume of oxygen | 3 | m3
Pipe | Pipe diameter | 9.5 | mm
 | Pipe length inside container | 45 | m
 | Pipe length outside container | 6 | m
 | Fuel cell pressure | 9 to 2 | bar
 | Electrolyser pressure | 40 | bar
Container | Free volume | 20 | m3
 | Ambient temperature | 288 | K

## Slide 9: ARAMIS – APPLICATION
Identification of accident scenarios
  1. Selection of the potential hazards present in this application.
    Hydrogen
    oxygen
  2. For all of those substances, identification of the potential hazardous equipment
    Pipe
    Electrolyser
    Fuel cell
    Storage, …
  3. Selection of the critical event, also called central event defined as a loss of containment
    Small leak
    Large leak
    Collapse of capacity
    …
Scenario :
Small leak on a pipe in the container

## Slide 10: BUILDING OF THE BOW-TIE
Small H2 leak
CENTRAL EVENT

## Slide 11: BUILDING OF THE BOW-TIE
Small H2 leak
OR
Small H2 pipe leak
Process overpressure
OR
Valve or component blocked
Failure of the cooling function
Internal overpressure
Mechanical attack
(Ageing…)
Leak on joint...
OR
CREATION OF THE FAULT TREE

## Slide 12: BUILDING OF THE BOW-TIE
Small H2 leak
OR
Mechanical attack
(Ageing…)
Small H2 pipe leak
Process overpressure
OR
Valve or component blocked
Failure of the cooling function
Internal overpressure
Leak on joint...
OR
Jet fire
Ignition
CREATION OF THE EVENT TREE
PhD n°2
PhD n°1
VCE
Delayed ignition
H2 accumulation

## Slide 13: BUILDING OF THE BOW-TIE
Small H2 leak
OR
Ignition
No hazardous phenomena
Mechanical attack
(Ageing…)
Small H2 pipe leak
Process overpressure
OR
Valve or component blocked
Failure of the cooling function
Internal overpressure
Leak on joint...
OR
Jet fire
Detection of overpressure in the process
Pressure relief valve
H2 detection in the container (threshold set at ¼ of H2-air LFL)
INSERTION OF THE SAFETY BARRIERS
VCE
Delayed ignition
H2 accumulation

## Slide 14: ESTIMATION OF PROBABILITIES
Small H2 leak
OR
Ignition
No hazardous phenomena
Mechanical attack
(Ageing…)
Small H2 pipe leak
Process overpressure
OR
Valve or component blocked
Failure of the cooling function
Internal overpressure
Leak on joint...
OR
Jet fire
10-5
10-2
2.10-7
2.10-5
1
Frequencies = orders of magnitudes
10-2
10-1
10-2
10-5
10-5
Ignition probability is equal to 1 (ignition happens in all of cases)
VCE
Delayed ignition
H2 accumulation
Only the fully developed dangerous phenomena are taken into account
Ignition of an explosive atmosphere from a small leak in the container > Probability = 10-7

## Slide 15: ESTIMATION OF PROBABILITIES
Small H2 leak
OR
Ignition
No hazardous phenomena
Mechanical attack
(Ageing…)
Small H2 pipe leak
Process overpressure
OR
Valve or component blocked
Failure of the cooling function
Internal overpressure
Leak on joint...
OR
Jet fire
10-7
2.10-5
Hazardous phenomenon studied next
Small H2 leak
Ignition
Jet fire
VCE
Delayed ignition
H2 accumulation

## Slide 16: ESTIMATION OF CONSEQUENCES
For a small leak (10% of pipe diameter – ø=0,9mm/P=40b)
  Most likely hazardous phenomena = immediate ignition of jet
    Jet fire (thermal effects) > model of Houf and Schefer (2007)
    Explosion of jet (overpressure effects) > Multi-Energy Method
  The characteristics of the jet :
    a supersonic release
    a mass flow rate of 1,64*10-3 kg/s
    the flame length is 2.2 m
Effect |  | Distance | 
Explosion | Thermal | Explosion | Thermal
20mbar | 1.8 kW/m² | 10 m | 1.6 m
50mbar | 3 kW/m² | 5 m | 1.3 m
140mbar | 5 kW/m² | 2 m | 1 m
200mbar | 8 kW/m² | 2 m | 0.8 m
Possible effects inside the container but no effect outside

## Slide 17: Probability classes Class of consequences
Definition of consequences class used in the case of a containerized hydrogen application
Probability | Quantitative estimation (per year) | Qualitative estimation
Improbable | < 10-5 | Possible but extremely unlikely event
Extremely rare | 10-4 to 10-5 | Very improbable event
Rare | 10-3 to 10-4 | Improbable event
Possible | 10-2 to 10-3 | Likely event
Occasional | > 10-2 | Common event
Ranking | Definition
C1 | Light effect inside
C2 | Moderate to Important effect inside, no effect outside
C3 | Important effect inside and light effect outside
C4 | Important effect outside, leading to dominos effects

## Slide 18: Risk Matrix; frequencies and consequences classes
Critical scenarios >
Potential effects outside
Mitigation strategies >

## Slide 19: DISCUSSION
ARAMIS methodology can be implemented, however, some limitations may jeopardize its usefulness.
  The frequencies depend very much on the past experience of incidents, defaults or accidents.
    The available databases do not represent the state of the art of the technology
  A similar comment about the classes of consequences.
    Available accident database is limited and may not represent the state of the art
    Consequences models take in account process and/or environmental conditions (Potential domino effects on/from the container would have to be considered)
  Again a “strong” demonstration of the safety is required for hydrogen-energy >
    Independency of the barrier; Failure on demand rate; Response time; Efficiency

## Slide 20: CONCLUSION
Using and adapting the ARAMIS method permits to use a demonstrative method and to incorporate and to take into account the safety barriers.
  Identification of all conceivable major accident scenarios
  Inventory of all safety equipment or barriers impeding the development of an accident,
  Generic calculation of the frequencies via the bow-ties.
The current databases (of frequencies and consequences) are unsuitable for the hydrogen applications.
The central character of the barriers is not sufficiently rested on, and particularly the assessment of efficiency (level of reduction) of the safety barriers.

## Slide 21: CONCLUSION
Future works:
  Calculation of the frequencies via a generator of probabilities with more detailed bow-ties
  Establishment of a specific database to hydrogen gathering information on initiating events probabilities
  Work on the criteria evaluation of the barriers in order to assess their influence on both frequencies and consequences. For example the evaluation of the barriers can be based on the evaluation of independence of barriers and the probabilities of failure on demand.
  Finally the calculations of the effects should also be reviewed in order to have a better estimation of the consequences knowing the conditions of use.
    Experiments in progress about jet explosions in obstructed area and vented deflagrations with turbulent flammable mixtures

## Slide 22: THANK YOU FOR YOUR ATTENTION
Audrey DUCLOS,
PhD Student
Research engineer
AREVA Energy Storage
Audrey.duclos@areva.com
Engineering Safety in Hydrogen-Energy Applications

## Slide 23
Small H2 leak
OR
Ignition
No hazardous phenomena
Mechanical attack
(Ageing…)
Small H2 pipe leak
Process overpressure
OR
Valve or component blocked
Failure of the cooling function
Internal overpressure
Leak on joint...
OR
Jet fire
Pressure relief valve
Detection of overpressure in the process
H2 detection in the container (threshold set at ¼ of H2-air LFL)
VCE
Delayed ignition
H2 accumulation