## Slide 1
An analysis of the experiments carried out by HSL in the Hyindoor European project studying accumulation of hydrogen released into a semi-confined enclosure in real wind conditions, and comparison with existing analytical models
2015 October, 20th
ICHS 2015 – Yokohama, Japan | ID195
Deborah Houssin-Agbomson, Simon Jallais

## Slide 2
Content
Context
Description of the experimental setup
Data selection
Results
Conclusions

## Slide 3
I. Context

## Slide 4: Context of the study
Risk assessment for H2 applications
Natural ventilation through dedicated opening(s) is an effective mean to limit hydrogen build-up in case of accidental release in a confined space
Validated approaches enable to evaluate hydrogen maximal concentration reached at steady state for ideal conditions of use
  e.g. Linden (1999), Woods et al. (2003), Molkov et al. (2013), Lowesmith et al. (2007)
But what about assessment approaches and safety strategies on H2 accumulation mitigation for H2 energy applications used in specific conditions?
Objectives of the study
  What is the effectiveness of ventilation apertures according to their configuration (location, number, type)?
  What is the potential impact of wind on hydrogen build-up when H2 applications are used outdoor?
  Are simple analytical approaches always available and accurate?

## Slide 5
II. Description of the experimental test bench

## Slide 6: HSL experimental test bench
Characteristics of the enclosure
  Dimensions: H2.5 x W2.5 x L5 m
  Internal volume: 31 m3
  Openings available for natural ventilation: up to 6
  Ventilation surface: 0.224 m2 each
Injection source
  Releasing gas: hydrogen at 50 cm from the ground
  Geometry: circular
  Internal diameter: 10 mm
  Releasing flow rate: from 150 to 1200 NL.min-1

## Slide 7: HSL experimental test bench
Ventilation openings
  Total: 6 apertures
    Five rectangular: H0.27 x W0.83 m
    One circular on the roof with chimney and rain protection cover
  One- and two-openings ventilation can be studied
  Influence of vent distribution can be studied too
Measurement devices
  Twenty seven electrochemical cell oxygen sensors
  Located at heights of 1 m, 1.75 m and 2.25 m
  Hydrogen maximal concentration deduced
  Hydrogen distribution according to altitude not available

## Slide 8
III. Data selection

## Slide 9: Data selection
HSL experiments
  Performed in the framework of the Hyindoor collaborative and EU funded project
  28 experimental configurations carried out
  But by analyzing these experiments, some skeptical points:
    On the steady state of some experiments
    On the stability and the accuracy of the measurements
Measurements at 2.25 m
Steady state not reached
Measurements not stable
 Two criteria were determined to perform a more drastic selection of the experiments for the study ot the wind influence on hydrogen build-up in real weather conditions  13 experiments retained

## Slide 10: Selected data
One-opening configurations
  7 experiments retained
Exp | Open top vents | Flow rate (NL.min-1) | Corrected wind velocity Eq.(1) (m.s-1) | Vent exposed | Steady state H2 (%)
1 | Two top vents on opposite side | 150 | 1.52 | Top vent | 0.7
3 | Two top vents on opposite sides | 300 | 0.00 | Top vent | 2.9
4 | Two top vents on opposite sides | 150 | 2.18 | Top vent | 0.6
6 | Two top vents on opposite sides | 600 | 2.26 | Top vent | 3.0
7 | One top vent | 150 | 2.60 | Top vent | 2.8
9 | One top vent | 250 | 0.00 | None | 11.6
20 | Chimney | 130 | 1.94 | Chimney | 8.1

## Slide 11: Selected data
Two-openings configurations
  6 experiments retained
Exp | Open vents | Flow rate (NL.min-1) | Corrected wind speed (m.s-1) | Exposed vent | Steady State H2 concentration
10 | Two top vents on opposite sides and one at the bottom | 800 | 0.78 | Top | 4.4%
14 | One top vent and one bottom on the opposite side | 1000 | 1.41 | Top | 5.9%
17 | Chimney and near bottom vent (vent 3) | 800 | 1.27 | Chimney | 8.9%
18 | Chimney and opposite bottom vent (vent 4) | 800 | 2.25 | Chimney | 5.5%
21 | Chimney and opposite bottom vent (vent 4) | 923 (sonic) | 2.22 | Chimney | 5.4%
22 | Chimney and opposite bottom vent (vent 4) | 887 | 2.37 | Chimney | 6.7%

## Slide 12
IV. Results

## Slide 13: Results | Analytical approaches for H2 values calculation
Selected experimental data were compared to several theoretical models implemented in Air Liquide in-house tools, so-called ALDEA (Air Liquide Dispersion and Explosion Assessment tools  ALDEA-CL3 and ALDEA-CL2
Experimental hydrogen maximal concentration measured at steady state were compared to calculated values
ALDEA-CL3 Based on Linden approach considering only the buoyancy of H2-air mixture inside the enclosure It could be used for calculations in one- or two-openings natural ventilation configurations Does not take into account wind
ALDEA-CL2 Based on Lowesmith works (2007) and takes into account the buoyancy and also the effects of the wind It has been validated in real conditions for H2-CH4 mixtures and real atmospheric conditions of reinforcing wind (NaturalHy project), and also validated for H2 against lots of experiments Lowesmith approach has to be used for “two-openings” ventilation mode

## Slide 14: Results | “One vent” configurations
Comparison between experimental data and calculated values
  Opposing wind
 ALDEA-CL3 largely overestimates hydrogen concentration compared to experiments in presence of wind
 Positive effects of wind on mitigation of hydrogen build-up which are not translated in the Linden approach
 Due to its design, chimney not affected by wind

## Slide 15: Results | “Two vents” configurations
Comparison between experimental data and calculated values
  Opposing wind
 ALDEA-CL3 and ALDEA-CL2 overestimate experimental measurements of hydrogen concentration
 Positive influence of wind on mitigation
 Difficulty to correctly evaluate concentration in presence of wind even with the Lowesmith approach
 Low wind velocity has no influence on chimney configurations, but high wind contributes positively to mitigation

## Slide 16
V. Conclusions

## Slide 17: Conclusions
Main conclusions
  This study showed the complexity to realize large scale experiments in real conditions due to quick variability of meterological conditions – specially for the wind
  In the conditions investigated, wind has always a positive impact leading to a decrease of hydrogen build-up compared to no-wind conditions, whatever the configurations of the openings for the natural ventilation; wind participates to the hydrogen build-up mitigation
  ALDEA-CL3 (Linden approach, without wind consideration) overestimates hydrogen build-up for “one-” and “two-openings” ventilation mode compared to experiments in real weather conditions
  ALDEA-CL2 (Lowesmith approach, enabling wind consideration) overestimates hydrogen build-up for “two-openings” ventilation mode compared to experiments in real weather conditions
  Wind effects are minimized for the configurations using a chimney as top vent; effects of wind are very limited due to the orientation of this ventilation aperture. Thus the ALDEA tools are in good agreement with these experimental cases

## Slide 18: Conclusions
Recommendations
  It seems to be not necessary, even unproductive, to protect from wind Hydrogen Energy applications since wind has shown a positive effect on hydrogen mitigation in conditions addressed by the HSL-Hyindoor experiments
  Actual analytical tools and methods, employed for risk assessment or design support – i.e. ALDEA-CL3 and ALDEA-CL2 – can be used since it is here shown that these approaches are conservative

## Slide 19: Acknowledgement
The experimental results presented in this communication have been obtained by HSL within the frame of the Hyindoor project The authors acknowledge the FCH-JU and the Hyindoor project partners

## Slide 20
An analysis of the experiments carried out by HSL in the Hyindoor European project studying accumulation of hydrogen released into a semi-confined enclosure in real wind conditions, and comparison with existing analytical models
2015 October, 20th Deborah Houssin-Agbomson, Simon Jallais
ICHS 2015 – Yokohama, Japan | ID194
Thanks for your attention
deborah.houssin@airliquide.com