## Slide 1: Venting deflagrations of local hydrogen-air mixture
D. Makarov1, V. Molkov1, P. Hooker2 and M. Kuznetsov3
1 HySAFER Centre, University of Ulster, Newtownabbey, BT37 0QB, UK
2 Health and Safety Laboratory, Harpur Hill, Buxton, SK17 9JN, UK
3 Karlsruhe Institute of Technology, 76344 Eggenstein-Leopoldshafen, Germany
6th International Conference on Hydrogen Safety 19-21 October 19-21, Yokohama, Japan

## Slide 2: Motivation
Available vent sizing methodologies are applicable only to uniform fuel-air mixtures occupying the whole enclosure
Deflagration of non-uniform or layered mixtures can generate overpressure above that for uniform mixture deflagration (the same amount of hydrogen)
Maximum overpressure depends strongly on portion of mixture with largest hydrogen concentration
Experimental data (FCH-JU HyIndoor project) recently became available for validation of the previously developed theory (Molkov, DSc thesis,1996)

## Slide 3: Layered mixture
Initial volume fraction of unburnt mixture
Volume fraction of fuel in combustible mixture
Calculation scheme

## Slide 4: Problem formulation
Volume conservation (non-dimensional form)
Mass conservation (non-dimensional form)
where A – fraction of vent area occupied by burnt mixture
Internal energy conservation equation
Mass outflow rate
where pi – initial (ambient) pressure, m – discharge coefficient, F – vent area
Ref.: V. Molkov, DSc thesis, 1996

## Slide 5: Model development
Expressions for internal energy:
Non-dimensional pressure (using perfect gas law and adiabatic process assumptions):
where  - density,  – non-dimensional (relative) density
from which it follows that

## Slide 6: Model development
Using thermodynamic relations
          - expansion coefficient
energy equation becomes

## Slide 7: Pressure dynamics
Introducing burning velocity
- non-dimensional time,
- venting parameter
- non-dimensional number characterising subsonic outflow

## Slide 8: Gas generation-outflow balance
General expression for gas generation-outflow balance, subsonic velocity
- dimensionless pressure
- mass fraction of unburnt mixture inside enclosure
- flame wrinkling factor

## Slide 9: Assumptions and simplifications
MAX overpressure (for relatively small pressures)
Fresh mixture at outflow
For low fuel concentrations
Vol. fraction of combustion process (completed combustion, adiabatic compression)
Expanding in Taylor series around :
,
For adiabatic compression
Low pressures, lean mixtures
Substituting , Z and in equation for W:
Eventually, expression for MAX overpressure

## Slide 10: Further derivations
Physical consideration:
Mass fraction of combustible fuel-air mixture
Mass of air in localised hydrogen-air mixture
Expression for vol. fraction of fuel-air mixture 

## Slide 11: Correlation
Final model formulation:
Correlation will be sought in the form similar to uniform mixture correlation:
where

## Slide 12: Deflagration-outflow interaction /
Treated similar to Molkov V., Bragin M., Hydrogen-air deflagrations: vent sizing correlation for low-strength equipment and buildings, in Proc. ICHS 2013, 9-11 September 2013, Brussels, Belgium
- wrinkling factor due to flame front generated turbulence
- wrinkling due to leading point factor
- wrinkling fractal increase of flame surface area
- wrinkling factor to account for initial turbulence
- increase of flame area due to enclosure elongation
- factor to account turbulence in presence of obstacles

## Slide 13: Experimental programme
Experiments at KIT (Germany)
L×H×W=0.98×1.00×0.96 m
Openings: from 0.10×0.10 m to 0.50×0.50 m
Spark ignition: at the rear plate centre or at the rear of top plate
24 tests: 10 uniform layer tests (=0.25-0.50, =0.10-0.25), 14 gradient layer tests (up to =0.20)

## Slide 14: Experimental programme
Experiments at HSL (UK)
L×H×W=2.5×2.5×5.0 m (volume 31.25 m3)
Openings: vents 1 and 5, total area 0.448 m2
AC spark ignition: 0.3 m under ceiling, 0.8 m from end wall
3 tests with non-uniform hydrogen layers (up to =0.123)

## Slide 15: Gradient layers
Maximum overpressure depends only on portion of mixture with largest hydrogen concentration
Analytical expression for overpressure is function of unburnt mixture volume fraction F
F is calculated taking into account only fraction of total hydrogen volume with the highest burning velocity
Mixture |  |  | Sui, m/s | Ei | cui, m/s | Dp1/Dp2
1 | 0.1 | 0.2 | 0.862 | 5.52 | 381 | 112.4
2 | 0.2 | 0.1 | 0.117 | 3.50 | 361 | 
Theory background

## Slide 16: Gradient layers
Example of gradient layer account
KIT tests with Gradient 1 (HIWP3-033, HIWP3-046):
Based on total hydrogen conservation: =0.55
Based on burning velocity range (0.95 – 1.0)SuMAX : =0.037
Layer =0.55 (hydrogen conservation)
Hydrogen distribution

## Slide 17: Correlation results
(shaded – non-uniform layer results)
 | Experiment | , % (vol.) | , % (vol.) | Ei | Sui, m/s | K | LP | F | AR | / | Brt-1 |  | Dpexp | Dpcorr
1 | HIWP3-032 | 9.00 | 9.8 | 3.47 | 0.095 | 1.42 | 2.32 | 1.89 | 1.46 | 9.1 | 1.81 | 0.568 | 3.5010-3 | 1.0110-2
2 | HIWP3-033 | 3.71 | 11.8 | 3.90 | 0.138 | 1.67 | 2.20 | 1.62 | 1.93 | 11.5 | 3.66 | 0.356 | 8.4010-3 | 7.7110-3
3 | HIWP3-034 | 2.71 | 14.8 | 4.53 | 0.336 | 2.04 | 2.03 | 1.40 | 2.08 | 12.1 | 10.32 | 0.337 | 2.1710-2 | 1.8310-2
4 | HIWP3-035 | 2.71 | 16.8 | 4.92 | 0.508 | 2.26 | 1.92 | 1.30 | 2.00 | 11.3 | 15.51 | 0.365 | 2.5810-2 | 3.1510-2
5 | HIWP3-036 | 2.71 | 16.8 | 4.92 | 0.508 | 2.26 | 1.92 | 1.30 | 2.00 | 11.3 | 15.51 | 0.365 | 2.4010-2 | 3.1510-2
6 | HIWP3-037 | 2.66 | 16.8 | 4.91 | 0.504 | 2.26 | 1.92 | 1.30 | 2.02 | 11.4 | 15.51 | 0.360 | 2.5510-2 | 3.0810-2
7 | HIWP3-038 | 2.81 | 19.8 | 5.48 | 0.804 | 2.59 | 1.76 | 1.20 | 1.88 | 10.3 | 23.69 | 0.415 | 3.0910-2 | 6.0610-2
8 | HIWP3-041 | 2.71 | 16.8 | 4.92 | 0.508 | 2.26 | 1.92 | 1.30 | 2.00 | 11.3 | 15.51 | 0.365 | 2.1010-2 | 3.1510-2
9 | HIWP3-042 | 2.71 | 16.8 | 4.92 | 0.508 | 2.26 | 1.92 | 1.30 | 2.00 | 11.3 | 15.51 | 0.365 | 3.0310-2 | 3.1510-2
10 | HIWP3-043 | 2.66 | 16.8 | 4.91 | 0.504 | 2.26 | 1.92 | 1.30 | 2.02 | 11.4 | 15.51 | 0.360 | 2.9610-2 | 3.0810-2
11 | HIWP3-044 | 2.71 | 14.8 | 4.53 | 0.336 | 2.04 | 2.03 | 1.40 | 2.08 | 12.1 | 10.32 | 0.337 | 2.8710-2 | 1.8310-2
12 | HIWP3-045 | 9.00 | 9.8 | 3.47 | 0.095 | 1.42 | 2.32 | 1.89 | 1.46 | 9.1 | 0.07 | 0.568 | 4.8010-4 | 4.9210-4
13 | HIWP3-046 | 3.71 | 11.8 | 3.90 | 0.138 | 1.67 | 2.20 | 1.62 | 1.93 | 11.5 | 0.15 | 0.356 | 3.5010-4 | 3.7410-4
14 | HIWP3-047 | 2.71 | 14.8 | 4.53 | 0.336 | 2.04 | 2.03 | 1.40 | 2.08 | 12.1 | 0.41 | 0.337 | 5.2010-4 | 8.8910-4
15 | HIWP3-072 | 25.0 | 10.0 | 3.50 | 0.104 | 1.44 | 2.31 | 1.86 | 1.24 | 7.7 | 0.07 | 1.134 | 1.0810-3 | 1.8610-3
16 | HIWP3-073 | 50.0 | 10.0 | 3.50 | 0.104 | 1.44 | 2.31 | 1.86 | 1.24 | 7.7 | 0.07 | 1.323 | 2.4010-3 | 2.5210-3
17 | HIWP3-074 | 25.0 | 15.0 | 4.56 | 0.350 | 2.06 | 2.02 | 1.39 | 1.24 | 7.1 | 0.26 | 1.491 | 4.5210-3 | 1.1210-2
18 | HIWP3-075 | 50.0 | 15.0 | 4.56 | 0.350 | 2.06 | 2.02 | 1.39 | 1.24 | 7.1 | 0.26 | 1.510 | 1.4310-2 | 1.1410-2
19 | HIWP3-076 | 25.0 | 20.0 | 5.52 | 0.826 | 2.61 | 1.75 | 1.19 | 1.24 | 6.8 | 0.64 | 1.661 | 2.6610-2 | 3.2810-2
20 | HIWP3-077 | 25.0 | 20.0 | 5.52 | 0.826 | 2.61 | 1.75 | 1.19 | 1.24 | 6.8 | 0.64 | 1.661 | 2.5810-2 | 3.2810-2
21 | HIWP3-078 | 50.0 | 20.0 | 5.52 | 0.826 | 2.61 | 1.75 | 1.19 | 1.24 | 6.8 | 0.64 | 1.661 | 6.2710-2 | 3.2810-2
22 | HIWP3-079 | 25.0 | 25.0 | 6.36 | 1.24 | 2.32 | 1.52 | 1.07 | 1.24 | 4.70 | 0.72 | 1.783 | 6.2610-2 | 4.2010-2
23 | HIWP3-081 | 50.0 | 20.0 | 5.52 | 0.826 | 2.61 | 1.75 | 1.19 | 1.24 | 6.76 | 0.64 | 1.661 | 7.9010-2 | 3.2810-2
24 | HIWP3-082 | 50.0 | 25.0 | 6.36 | 1.24 | 2.32 | 1.52 | 1.07 | 1.24 | 4.70 | 0.72 | 1.783 | 1.8310-1 | 4.2010-2
25 | WP3/Test22 | 22.0 | 12.3 | 4.00 | 0.197 | 1.73 | 2.18 | 2.69 | 1.32 | 13.3 | 1.11 | 1.196 | 5.0010-2 | 2.8310-2

## Slide 18: Correlation results
Best fit
Best fit achieved for A=0.018, B=0.94 :

## Slide 19: Conclusions
The analytical model for vented deflagration of localised mixtures, its major assumptions and derivation steps were presented
The model analysis and comparison with experiments proved that only a small fraction of the non-uniform mixture with highest burning velocity will have effect on the maximum overpressure
The technique to calculate this fraction of unburnt mixture in non-uniform layers accounted mixture with burning velocity within the range between 95% and 100% of the maximum burning velocity
The model has a potential to be used for hazards analysis and design of mitigation measures against deflagrations of realistic non-uniform mixtures in context of safe indoor use of hydrogen applications

## Slide 20
Thank you for your attention!
The research was supported through FCH-JU “HyIndoor” project, grant agreement No. 278534, www.hyindoor.eu