## Slide 1
Toshio Mogi, Woo-Kyung Kim, Ritsu Dobashi
The University of Tokyo
Fundamental study on accidental explosion behavior of hydrogen/ air mixtures in open space
ICHS 2011
International Conference on Hydrogen Safety
September 12-14, 2011
San Francisco, California-USA
1

## Slide 2: Background
Hydrogen
Low ignition energy (0.019mJ)
Extensive flammable region (4-75vol%)
Easy leakage and high diffusivity
Clean energy carrier Renewable energy
Expected as an alternative fuel ( ex. fuel-cell vehicle)
Properties on safety
Hydrogen filling station
If hydrogen leaks from hydrogen handling system,
electrostatic spark discharge
serious fire and/or explosion accidents.
2

## Slide 3: Background
K. Wakabayashi, et al, 1st ICHS, 2005
M. Groethe, et al, 1st ICHS, 2005
To evaluate the strength of hydrogen/air mixture explosion, unconfined large scale experiments were recently carried out.
However, there has been little systematic research on the relation between flame propagation and blast wave in unconfined space.
Hazard analysis on an accidental explosion is very important.
Gas explosion causes indeed serious damages.
3

## Slide 4: Objectives
To understand the relation between flame propagation and blast wave in open space
Hydrogen/air deflagration experiment using soap bubble method
The effect of hydrogen/air mixture concentration to behavior of flame propagation and blast wave
4

## Slide 5: Experimental setup
Gas supplying system
Ignition system
High speed Schlieren photography system
Sound pressure measuring system
5

## Slide 6: Detail of Schlieren pictures
Before ignition
After ignition
Bubble surface
Insulator
Electrode
Nozzle
Bubble surface
Flame front
Boundary between
mixture and surrounding air
6

## Slide 7
Movie (f = 1.8 )
7

## Slide 8
Flame propagation at equivalence ratios of 0.7, 1.0, 1.8.
Time
f
8

## Slide 9
Flame propagation at equivalence ratios of 2.5, 3.0, 4.0.
f
Time
9

## Slide 10: Flame radius versus time at various equivalence ratios
ru: initial soap bubble radius
rb: burned flame radius
Mean burning velocity calculation
10

## Slide 11: Comparison between measured mean burning velocity and literature data
11

## Slide 12: Pressure wave histories with different equivalence ratio
12

## Slide 13: Comparison with existing simple model
The blast overpressure at the position d from the explosion point is equated by the theory of acoustics;
p : pressure
t : time
dV/dt : volumetric rate of combustion
A.Thomas et al. (Proc. R. Soc. Lond. A 294: 449-466 ,1966)
Theory of acoustics
S : burning velocity
e : volumetric expansion ratio
rq : flame radius at quenching
ｒ
e S
13

## Slide 14: Comparison between measured and predicted peak overpressure
14

## Slide 15: Discussion-Existing study on blast wave at acceleration of flame propagation
e S
ｒ
Laminar flame propagates spherically
S : burning velocity
e : volumetric expansion ratio
rq : flame radius at quenching
S=constant
A.Thomas et al. (Proc. R. Soc. Lond. A 294: 449-466 ,1966)
15

## Slide 16: Time histories of flame radius, burning velocity, overpressure (f = 0.7)
≠constant
16

## Slide 17: Time histories of flame radius, burning velocity, overpressure (f = 1.8)
17

## Slide 18: Time histories of flame radius, burning velocity, overpressure (f = 3.0)
18

## Slide 19: Discussion Diffusive-Thermal instability(Lewis number)
stable
unstable
Unburned
side
Burned
side
Mass diffusion
Heat diffusion
(Le>1,stable)
Unburned
side
Burned
side
(Le<1,unstable)
19

## Slide 20: Discussion Different type of wrinkled flame
f = 0.7
f = 4.0
Diffusive-thermal instability
Wrinkled flame by rupture of a soap bubble
wrinkled flame by the rupture of a soap bubble is related with
non-uniformity concentration distribution
20

## Slide 21: Conclusions
1) The measurements of the intensities of blast wave show that;
in lean hydrogen-air mixture the overpressure grew linearly with time
in rich hydrogen-air mixture the overpressure grew linearly with time in the early stage and acceleratingly increase in later stage.
The accelerating increase in the later stage resulted in a much larger peak overpressure than that in the stoichiometric mixture.
2) The overpressure of blast wave can be predicted by the acoustic theory if the real burning velocity could be known.
The theory indicates that the intensity of blast wave is affected by burning velocity, volumetric expansion ratio and flame acceleration.
In particular, the intensity of the blast wave is strongly affected by the acceleration of the burning velocity.
21

## Slide 22: Thank you for your attention!
mogi.toshio@mail.u-tokyo.ac.jp
22