## Slide 1: Non-adiabatic blowdown model: a complimentary tool for the safety design of tank-TPRD system
M. Dadashzadeh, D. Makarov, V. Molkov
Hydrogen Safety Engineering and Research Centre
7th International Conference on Hydrogen Safety
Hamburg, Germany, 11-13 September 2017

## Slide 2: Onboard storage
Objectives:
Reduce TPRD diameter to avoid:
  Large flame length of hydrogen jet fire
  Pressure peaking phenomena to prevent civil structure demolition
Exclude tank rupture during blowdown in a fire when TPRD orifice size is small
Optimizing tank-TPRD system performance

## Slide 3: Ulster model
Problem formulation: tank in a fire
TPRD
q"
Phenomena (heating only):
Heat transfer from the fire through the wall to stored gas
Temperature and pressure of gas increase
Load-bearing thickness of the wall increases from inside
Material decomposition wave propagates from outside
Rupture: load-bearing thickness “meets” decomposition wave
: Heat flux from the wall to stored gas

## Slide 4: Ulster model
Problem formulation: tank in a fire with TPRD
Additional phenomena (cooling due to TPRD activation):
Pressure and temperature decrease
Wall load-bearing thickness decreases
Heat transfer from cooled gas to the wall (cold wave)
Wall decomposition wave may slow down or even stops
Rupture is delayed or prevented
TPRD activated

## Slide 5: Ulster model
Equations, input, output
Formulation |  | 
TPRD-tank system | Equation | Reference
Gas | Energy conservation equation Real gas EOS (Abel-Noble) | Molkov et al., 2009 Johnson, 2005
Notional nozzle | Under-expanded jet theory | Molkov et al., 2009
Tank | 1D unsteady heat transfer equation Nu correlations for convective heat transfer Enthalpy change during decomposition* | Patankar, 1980 Woodfield, 2008 Voller, 1985
Input |  | 
Tank and hydrogen properties; external heat flux; TPRD diameter and initiating time |  | 
Output |  | 
Gas pressure and temperature; tank wall temperature; time to rupture or blowdown time |  | 
Wall material decomposition is not considered at the current stage of this study but it is under investigation for the further development of the model

## Slide 6: Ulster model validation
Test by KIT: 19 L Type IV tank; Helium; Pressure 70 MPa
TPRD diameter 1 mm
Theory by Ulster
Tank material parameters: Acosta et al., 2014; Welch et al., 2017
Pressure: adiabatic vs non-adiabatic model

## Slide 7: Ulster model validation
Test by KIT: 19 L Type IV tank; Helium; Pressure 70 MPa
TPRD diameter 1 mm
Theory by Ulster
Tank material parameters: Acosta et al., 2014; Welch et al., 2017
Temperature: adiabatic vs non-adiabatic model

## Slide 8: Ulster model validation
Thermocouple shielded with magnesium oxide and thin steel shell: KIT, 2017
Top metal plate is steel 1.4571: KIT, 2017
Lump heat transfer model, considering the metal plate is thermally thin
Nu correlations for convective heat transfer: Incropera et al., 1985
Metal plate properties: www.engineeringtoolbox.com
Temperature: thermocouple response delay

## Slide 9: Ulster model validation
Test by KIT: 19 L Type IV tank; Helium; Pressure 70 MPa
TPRD diameter 1 mm
Theory by Ulster
Tank material parameters: Acosta et al., 2014; Welch et al., 2017
Temperature: adiabatic vs non-adiabatic model

## Slide 10: Concluding remarks
A model for design of inherently safer system TPRD-storage tank is formulated.
The model is validated against non-adiabatic blowdown (KIT test).
  Satisfactory agreement for dynamic pressure/temperature
The model validation against temperature and pressure rise in a tank in a fire (KIT test) is under development
The model can be applied for hydrogen safety engineering of a system TPRD-storage tank

## Slide 11
Thank you for your attention!